## Slide 1: A Basis of Design for Marinas Docks and Marinas™
Jack C. Cox, PE, BC.CE, BC.NE, BC.PE
Principal, Vice President of Engineering
Edgewater Resources

## Slide 2
A Basic Understanding of Waves and Currents

## Slide 3: Water Movement in a Wave
Depth of water compared to wavelength controls behavior
  H=1, T=4, D=15
  H=1, T=4, D=7
  H=1, T=4, D=3

## Slide 4: Wavelength: Water Depth Look-Up Table
Note: for common marina water depths and boating wave climates, the wavelength is roughly 80-100 ft.
2.0
2.5
3.0
3.5
4.0
4.5
5.0
5.5
6.0
6.5
7.0
5
19
27
38
41
48
54
61
67
74
81
87
10
20
31
42
52
63
73
82
92
102
111
120
15
21
32
45
58
71
84
96
108
121
132
144
20
21
32
46
61
76
91
106
121
135
149
162
25
21
32
46
62
79
96
113
130
146
162
178
30
21
32
46
62
81
99
118
136
155
173
190
35
21
32
46
62
81
101
121
142
162
181
200
40
21
32
46
62
81
102
123
146
167
188
209
Period
Depth
Deep Water Waves

## Slide 5: Water Movement in Rivers

## Slide 6: Understanding Rivers and Currents

## Slide 7: Design Considerations
Need to think about the full boater experience from outside the harbor to inside
  Approaching the marina
  Entering/leaving the marina
  Berthed in the marina
  Environmental quality

## Slide 8
Approaching and Entering the Marina

## Slide 9: Harbor Ingress/Egress Needs
Power Boats (Ingress)
  Poor steerage in following seas
  Align approach 25°- 35° off wave angle
Sailboats (Egress)
  Poor motive in head winds
  α >45°
Design marina approach using quartering seas
Do not require maneuvering turns through entrance –

## Slide 10: Recognize the Highest Safety Risk is in a Marina Entrance and Approach
Reduced speed/less maneuverability
Congested boat traffic zone
Natural and induced agitations from shore and structures

## Slide 11: Control Agitation at Entrances
Add wave absorption near entrance to limit reflections into approach channel.

## Slide 12: Protection Must be 3-Dimensional
Waves will bend (diffract) around structures and enter marina

## Slide 13: Protection Needs are Proportional to Wavelength
Generally, a structure needs to be at least 3 wavelengths wide to generate an economical shadow
  W=L/4
  W=L
  W=L/2

## Slide 14: Harbor Entrance Criteria
Waves < 3ft.
Currents < 3 knots tidal flow; 2.5 knots cross flow
Water depth > 10ft.
Boat orientation
  Quartering seas to ensure steerage
Note: Account for shoaling and sedimentation at entrance, which can trigger breaking of smaller waves

## Slide 15: Idealized Harbor Entrance
Approach into marina is not a beam sea
Straight approach, no turns required until inside breakwater shadow
Energy dissipation within harbor to reduce reflections impacting low speed operation
Offset access to berthing area
External diversion of sediments

## Slide 16: Best Practice Marina Examples
  Puerto los Cabos, Mexico
  North Point Marina, Illinois
  Quarters, Portugal
  Exmouth Boat Harbor, Australia

## Slide 17
Basin Tranquility

## Slide 18: Basin Agitation: Small Craft Berthing
USACE says:
10% of time = 2 weeks of seasonal marinas operation
= 5 weeks of all-season marinas operation
Criteria does not recognize significance of boat wakes, harbor chop or type of boating

## Slide 19: Basin Agitation: Small Craft Berthing
Note most stringent criteria occurs when the wave period is between 3 and 4 seconds
Wave Event Exceeded Once A Year |  |  |  | 
Vessel Length [m,(ft)] | Beam/Quartering Seas |  | Head Seas | 
 | Wave Period | Wave Height | Wave Period | Wave Height
 | [sec] | [m, (feet)] | [sec] | [m, (feet)]
4.0-10.1 (13-33) | < 2.0 | 0.21, (0.7) | < 2.5 | 0.21, (0.7)
 | 2.0 - 4.0 | 0.09, (0.3) | 2.5 – 4.0 | 0.15, (0.5)
 | > 4.0 | 0.15, (0.5) | > 4.0 | 0.21, (0.7)
10.1-15.8 (33-52) | < 3.0 | 0.24, (0.8) | < 3.5 | 0.30, (1.0)
 | 3.0 – 5.0 | 0.15, (0.5) | 3.5 – 5.5 | 0.21, (0.7)
 | >5.0 | 0.21, (0.7) | > 5.5 | 0.30, (1.0)
20.1 (66) | <4.0 | 0.30, (1.0) | < 4.5 | 0.30, (1.0)
 | 4.0 – 6.0 | 0.15, (0.5) | 4.5 – 7.0 | 0.24, (0.8)
 | > 6.0 | 0.24, (0.8) | > 7.0 | 0.30, (1.0)

## Slide 20: “Excellent” vs. “Good” vs. “Moderate” Berthing

## Slide 21
Design for Winds and Currents

## Slide 22: Slip Alignment with Wind/Current Affects Design Loads
  Effective area calculation
  True Drag Coefficient as Function of Direction
  Resultant force direction may NOT be same as application direction.

## Slide 23: Slip Alignment with Wind/Current Affects Design Loads
  Applied Load:
  F┴=b3F||

## Slide 24
Navigation Considerations

## Slide 25: Channel Width Requirements
Width measured at navigable depth

## Slide 26: Navigation: Basic Vessel Clearance Needs
2-Way Channel Widths
Wchannel
= 5Bmax (ideal conditions)
= 6Bmax (normal conditions)
= 9Bmax (poor conditions)
1- Way Traffic
W= 3Bmax
Boats moored along channel
W= Wchannel + 2Bmoored

## Slide 27: The “Why” For Channel Widths
Width of Sailing Lane: W = B + Δw
0.3B< Δw < 0.8B

## Slide 28: Navigation: Vessel Turning Capability
  Minimum turning radius for a vessel underway is 1.8 – 2.0L
  Note: Rudders stall for wheel angles > 40º
L

## Slide 29: Navigation: Steerage in Turns
Boats turn and steer similarly to cars while backing up

## Slide 30: Maneuvering in Bends
Channel Bends
  α<25º R= 3Ls
  25º<α<35º R=5Ls
  α>35º R=10Ls
  and
  ΔW = Ls2/8R
  For R = 4Ls & Ls/B = 4 , ΔW ≈ .125B
Bend deflection angles > 30º not recommended
ΔW
W
W

## Slide 31: Straight Segments Needed Between Curves
Straight segments of 5Ls should occur between each bend

## Slide 32
Approaches to Protection

## Slide 33: Understand the Form and Scale Needed to Provide Protection

## Slide 34: Balance Storm Wave Protection with Project Cost/Footprint Needs
  Basic Trapezoidal Breakwater Transmission
  Target: Freeboard = Hs
  Height of Breakwater above waterline controls transmission more than width

## Slide 35: Wave Attenuator Concepts

## Slide 36: Attenuator Types: Single Fence
  Swinging Panel
  Fixed Panel

## Slide 37: Attenuator Types: Double Fence (Pi)

## Slide 38: Wave Attenuator: Prisms

## Slide 39: Wave Power Transmission Past an Attenuator
HT = 23%
HT = 63%
5 ft.
Residual Power
= 40%
Residual Power
= 5%
HT = 23%
HT = 63%
4 Sec.
2 Sec.
3 ft.
10 ft.
Longer wave periods transmit more power under the barrier

## Slide 40: Storm Wave Protection to Meet Agitation Goals
Attenuator Geometry Equivalence:
  +1ft. Draft = +6ft. Breadth for 30% transmission
  Draft (D) > 15% of local wavelength & T < 3 sec for Ct < 50%:

## Slide 41: General Performance Expectations for a Floating Wave Attenuator
Attenuator Transmission Goal = Ct < 30%:
  Practically achievable only when T < 4 second periods (L < 100ft.)
  Effectiveness highly dependent on attenuator design
  Efficiency highly dependent on restraint design

## Slide 42: Wave Attenuator for Longer Periods

## Slide 43
Preserve Water Quality in the Marina

## Slide 44: Basin Proportions Control Flushing
E
Long and narrow basins flush poorly
EPA Recommended Flushing Time
  < 4 days = Good
  < 10 days = Acceptable
  > 10 days = Unacceptable

## Slide 45: Basin Shape Enhances Circulation
Water Quality Impact
  R < Minimum (L,W)/8 = Poor
  R > Minimum (L,W)/4 = Good

## Slide 46: Entrance Position and Number Affects Flushing

## Slide 47: Configure Your Marina for Efficiency, Security, Tranquility, High Quality, and Social Enjoyment
This? – Poor flushing, highly reflective, awkward layout
Or This? – Well flushing, calm water, efficient layout

## Slide 48: Contact Information
Jack C. Cox, PE, BC.CE, BC.NE, BC.PE
  Principal, Vice President of Engineering
  Edgewater Resources
  434 S Yellowstone Dr.
  Suite 203
  Madison, WI 53711
  608.716.3128 (office) 608.556.5377 (cell)
  jcox@edgewaterresources.com